## Slide 1: The Magic of the 3D Printer

## Slide 2
Creates Parts by extruding successive layers of plastic material
Virtually any complexity
Enclosed hollows are possible

## Slide 3: Evolution of the 3D Printer
- First ultra violet sintering of photoreactive polymer.
1987 - Stratasys patents FDM (Fusion Deposition Method)
- Stratasys patent expires. Reprap & Makerbot forge the DIY market.
2019 - Over 170 companies making 3D Printers.

## Slide 4: Examples: Functional Pieces
Star Light Holder
Offset Duct Connector
Parts Tray

## Slide 5: Examples: Fun Things
Oscillating Lever
Continuous Circulating Balls

## Slide 6: Examples: Odds & Ends
Spiral Vase
Enclosures
Ink Stamps

## Slide 7: Examples: Small Pieces
Pottery Stamps
Specialty Gear
Parts

## Slide 8: The 3 D Printer: Creality Ender 3 V2
FRONT
BACK

## Slide 9: Filament

## Slide 10: Filament Feeder

## Slide 11: Hot End

## Slide 12: Axis of Motion & Build Plate

## Slide 13: Build Plate Leveling

## Slide 14: Procedure to Print
1. Design part in CAD (either solids or surfaces).
Save as an .stl file.
Input to Slicer program.
Slice in layers and review.
Save on an SDmicro card, as a gcode file.
Place card into 3D Printer and select file to print.

## Slide 15: Printing Materials (Filaments)
PLA (Poly Lactate Acid) - Most Commonly Used:
A thermoplastic polyester.
Made from plant material, not petroleum oil.
From Starch, from corn, sugar beets, and sugar cane.
Hard, strong, brittle but not fragile.
Water soluble over long exposure times.
Many Colors.
ABS and PETG: Other Commonly Used
Nylon and TPU: Less Commonly Used:

## Slide 16: Print Variables (many others)
Extruding Layer Height - typical .2 mm~.008”
Wall Thickness - typical 1mm ~ .040”
Filler Between Walls - typical 20%
Accuracy - within a few thousandths
Shrinkage - relatively minimal

## Slide 17: Potential Problems
PLA Filament - Moisture Absorption (Heat filament 6 hr at 130 def F)
Adhesion to Build Plate (use glue stick)
Need for Support (use Supports in slicer)